## Slide 1: A Mobile Platform for Remote Inspection Inside ESRF Tunnel
A tool for minimizing the down-time
Jean-Michel Chaize
David Robinson
Laurent Hardy
Jouni Mattila
Antti Hahto
ESRF
Tampere University of Technology

## Slide 2: LabRat project
The context and the need
The project
Design features
Further development

## Slide 3: 24h operation over 7 days -> NO ACCESS
No way to do visual checks without cutting the beam
no beam cut shorter than one hour
  Heating time of the SR equipment
  Thermal stabilization time on beamlines optical elements
  Etc…

## Slide 4: Aging hardware -> Potential problems
Water alarms (pipes radiation damage)
Fire alarms (smoke, hot points…)
Temperature alarms (hot point due to beam)
Motor blocking (mechanical obstacle)
….

## Slide 5: Alarm occurrence: Is it a severe problem ?
  Small leak: we can wait and prepare an intervention at an adequate time.
  Big problem: it is better to prepare the intervention before cutting the beam
  Anyway, we have to cut the beam to check!

## Slide 6: Temperature problems need beam to show-up

## Slide 7: An autonomous robot could help us
  Wifi remote operation
  Color image transmission to CTRM
  Pan tilt zoom high quality video
    Movable arm for different point of view

## Slide 8: ESRF major constraints
  Should stay alive without human intervention for one week
    automatic recharging system
  Long travelling path (200m)
    Should be fast enough
  Narrow path (90 cm)
  Need several point of view for pan/tilt/zoom camera
    movable arm
  MTBF should be higher than Storage Ring!
  High level of radiation
    Shielding = 20Kg minimum for lead!

## Slide 9: Plethoric choice on the web
  Google search on “autonomous robot” give huge and various results…

## Slide 10: Commercial products
Many tools, market growing rapidly
We bought one!

## Slide 11: Learn from experience
Manual joystick remote operation is not sufficient
  WiFi coverage sometimes weak
  Video transmission freezing -> unsecure situation
  Very long travel become tedious.
We need far more than a remote operated car,
  The vehicle should be able to go to destination autonomously
  If WiFi interrupted-> Continue until target position reached
  Should take the best decision in case of unforeseen situation
Reliability is a real issue…
  Autonomy for at least one week.
Shielding missing, ->, +20Kg payload -> not possible on many devices
Limited facilities for localization
  No GPS, No active transponders, should learn form environment.
Need to be modular and extensible
  Infrared camera, radiation measurement etc…

## Slide 12: We do not have the necessary competences ->Collaborative project
Found a partner with high level of expertise in robotics
  Artificial intelligence, Virtual reality
  Remote handling
  Intelligency of mobile machine
  Mechanical design
  Is building a robot for ITER
Interdiciplinarity, cooperation industry,
technology transfer
The Target: Building a tool that can be reproduced and used in other institutes.

## Slide 13: LabRat project: general architecture

## Slide 14: Software architecture

## Slide 15: Graphical User Interface

## Slide 16: Current status
Mechanical platform working
  few improvement are necessary
Path planner software OK
On board camera OK
Automatic charging procedure in development
Commissioning of first prototype in November
  For remote observation.
  Need intensive tests before entering in the real tunnel…

## Slide 17: Further developments
Integration of various detectors
  X /Gamma radiation mapping
  Pyrometer
Automatic scanning
  Scan the tunnel volume with detectors
  Do periodical patrol planning
Improve the navigation system
  A navigation system based on stereovision
  Self learning…
A Tango device server to integrate it in the Control System
  Status, alarm, position etc…

## Slide 18: Conclusions
We are close to the first operational prototype.
Our aim is to have LabRat as a standard industrial product
Some R&D efforts still needed
  Possibility to obtain some public R&D funding from Finland
  For adjusting LabRat to synchtrotrons’ needs, R&D project
Looking for synchrotrons willing to test the product and partner in the development
Pls. contact: Jouni.Mattila@tut.fi or chaize@esrf.fr